## Slide 1: Digital Signal Processing Final project
2015, Lisbon

## Slide 2: Introduction
Additive synthesis
  reproduction of a given sound
  uses sine waves as basic function
  based on the Fourier-theory
  the given sound should be Fourier-transformed
    the k most relevant amplitudes and frequencies are collected
    the sound is estimated with the superposition of k sine waves with the given amplitudes and frequencies
  ADSR, filters, modulations and other basic functions are also implemented
  implementation in MATLAB

## Slide 3: Basic function
Requirements
  read the audio file
  do the Fourier-transformation
  sort the coefficients
  save the k most relevant amplitudes and frequencies
  compose and sum up the elementary sine waves
Test
  first with synthetic sounds
  later with records of real instruments

## Slide 4: Basic function
Results
  original sound is from The Prodigy – Voodoo people
  k = 10
  without ADSR, filters etc..

## Slide 5: Basic function
Results
  original sound is from The Prodigy – Voodoo people
  k = 500
  without ADSR, filters etc..

## Slide 6: Basic function
Results
  original sound is a piano sound
  k = 500
  without ADSR, filters etc..
  more complex sound with some reverb

## Slide 7: ADSR
A – attack time
D – decay time
S – sustain time and level setting is different in each case
R – release time

## Slide 8: ADSR
Results
  original sound is a flute sound
  k = 500
  with ADSR
  tremolo (modulation) in the end of the sound

## Slide 9: ADSR
Results
  original sound is from Benny Benassi – Satisfaction
  k = 4000
  with ADSR
  synthetic bass sound

## Slide 10: Different basic functions
instead of sine waves using
  square with changeable duty cycle -> odd-integer harmonics
  sawtooth -> all-integer harmonics
enrichement of the sound
  more content in frequency-domain
  essentially these basic functions are the totality of sine waves by the Fourier-theory

## Slide 11: Different basic functions
Results
  original sound is from Benny Benassi – Satisfaction
  k = 10
  with square basic functions
  synthetic bass sound

## Slide 12: Non-linear transformation
5 different transformation:
  ,
  where is the basic function
enrichement of the sound
  non-linearity produces more harmonic in frequency-domain

## Slide 13: Non-linear transformation
Results
  k = 100/200
without transformation

## Slide 14: Subtractive sound synthesis
using filters to shape the sound
  attenuation
  enhancement
chosen filter is Butterworth filter which is designed to have as flat a frequency response as possible in the passband.
  lowpass
  highpass
  bandpass

## Slide 15: Subtractive sound synthesis
Results
  k = 500
  with non-linear transformation
  with non-linear transformation